## Slide 1: Road Map for Space Harness
11
Marc Malagoli, Senior Expert in EWIS*, Electrical Architecture & Electrical Connectivity
marc.malagoli@airbus.com
16 October 2024
Vision and Opportunities for DC Harness Technologies
* Electrical Wiring Interconnection System

## Slide 2
Usual Vision of the Electrical System
A Monster is hiding there!
Image generated by AI

## Slide 3
Interconnections!

## Slide 4: The Visible part : The Harness
Up to 70 000 connections
100 to 250kg
Critical Schedule
Complex Accommodation & Installation
Hundreds of connectors
Complex and large PBC’s
Automation is not feasible for Space harness

## Slide 5: The Hidden Costs of Interconnection Complexity
Airbus Amber
Big efforts to Design, install and Validate Definition of Electrical Architectures, Units Interfaces, Spacecraft accommodation, Test procedures
Specific analyses: EMC, thermal control, high voltage, failure modes
Industrial Nightmare: Interfaces and interconnections require vast data, lots of stakeholders, and multiple iterations. On the critical path,
Performance penalties Mass, volume
Assembly & Tests: risks of damage, anomalies management
Huge cost spread on the whole project,
globally undocumented
Notes: Revoir

## Slide 6: The Vision
Dream of highly flexible electrical architectures,
enabling quick and cost-effective design for optimized space systems…
… Then develop building blocks to realize this vision
using commonplace ground technologies.

## Slide 7: The Dream
Minimal Connectivity
Enhanced Features

## Slide 8: Complex to Simple : the gains
Simplicity is the best way to achieve quality while reducing costs and lead times.
Simple to design
Less connectors on PBC’s
Re-USE Building Blocs
Easy to validate
Easy changes
EMC friendly
A few building blocs for lots of features
Low mass
Reduced Cost
Short Lead time
Improved performances
Modern technologies
More Reliable

## Slide 9: How - principles
Interconnections have Two primary uses
Power:
Connect Sources,
Distribute to electronics & Thermal Control
Data: Transfer Commands, Sensors, Payload Data
Electrical Unit
Power
Data bus
The “DC” electrical interface of most of the units
should look like this:
Interdependence
Notes: Revoir schéma

## Slide 10: Reconsider our architectures for low connectivity Some Guidelines
Moving functions to reduce interconnects:
Split or merge units.
Challenge the location of switching, protections, power and signal conditioning…
Make the units smart and autonomous (battery, equipment’s, actuators, heaters…)
Transitioning to fully digital on-board data transfer:
Onboard, data is often transmitted in analog form between units although it is eventually digitalized for computer and telemetry use.

## Slide 11: Thermal Control accounts for over 30% of the total interconnections
Thermal Control
Huge Total Cost of Ownership:
Complex Design
Lots of discrete components
High Installation workload & lead time
Need to seek further optimization between
Electrical, Mechanical and Thermal control systems
Other

## Slide 12
For every complex problem, there is a solution that is simple, obvious, and wrong *
* Freely inspired by a quote from H.L. Menken – Image generated by Human Intelligence
Why not Wireless ?

## Slide 13: "Less wires" does not necessarily mean “Wireless."
A “wireless” link is still an interconnection, and a costly one!
Some wireless drawbacks:
RF (e.g. Wifi, RFID…):
  Electro Magnetic Compatibility concerns
  Susceptibility to jamming, spying
  Coverage within the spacecraft (may need several transceivers or antennae)
Optical (e.g. LiFi):
  Field of view
  Limitation on bandwidth
  Number of channels
Wireless is NOT a universal solution for onboard data transfers,
but it might benefit specific uses, like mechanisms and appendices.

## Slide 14: Projections for Space Passive Components

## Slide 15: Transition from individual onboard signals to data bus transfers.
    Digitalization, a major trend since the '90s, remains a work in progress.
    Main gaps:
    Data digitalization
    To use digital sensors as far as possible.
    To digitalize more signals inside the units.
    To replace remaining relay boxes with solid-state components (Mosfets, LCL shall be generalized).
    On-Board Data Transportation
    Current data link offers are suboptimal, with numerous standards, inferior performance to ground-based state-of-the-art, high costs, and EMI sensitivity. (Mil-STD-1553, SpaceWire, LVDS, RSxxx, CAN…)
    Harness evolution should lower costs for faster, higher-volume data transmission.

## Slide 16: Expected Evolution on Passive Component
Less harness
  Connectors, splices,
  Cables, especially for signals
  Coax
  Fastening materials…
Less discrete elements
  Thermisters
  Heaters
  Relays
  Fuses
https://zoppasindustries.com/it/resistenze-elettriche-flessibili/
http://www.meas-spec.com/

## Slide 17: Photonic as a promising game changer
  A "one-size-fits-all" photonic solution could standardize all on-board end-to-end data transfers.
  The Photonic Standards should cover some passive components:
    Fibers
    Cables
    Connectors: internal & external, adaptor
    Fiber optic Flex
    Splitter, Coupler, Fan-out
    => GSTP “End-To-End On-Board Data Handling Architecture Based On Optical High-Speed Links” (Kick-off expected in November 2024).
    "RF over Fiber" technology
    is as well projected
    to replace coaxial links
Image generated by AI
Image generated by AI

## Slide 18: Expected Evolutions on Passive Component, Thermal Control & Structure
https://www.minco.com/minco-offers-heaters-with-embedded-sensors/
Simplified interfaces
  The unit's interface should be designed based on external connections to enable harness automation. E.g.:
    Try to limit to 2 connectors: 1 power + 1 data
    1 wire per contact, no splice, minimize shieldings
  More Fast lock connectors
  New building blocs, passive and/or active
  Smart hardware
    Smarter electronic units (integrated thermal control, digital interface)
    Smart heaters (active or passive including heaters + thermal regulation)
    Smart structures
      Embedded flat cables
      Embedded thermal control
      Embedded components
  New technologies
    Digital or photonic Sensors (thermal, strain, position…)
    MEMS
    Conductive printing,
    Additive manufacturing for conductors
Need of Standards

## Slide 19: Conclusion: Disruptive changes to come, Long Term, Support needed…
Our architectures are hampered by overly complex interconnections, leading to high costs, long lead times, and quality issues. Incremental changes to harness technologies without revising our systems and avionic won't provide major benefits.
We can drastically reduce this complexity by rethinking our systems, challenging each interconnection and using new components.
To achieve disruptive advancements, we should focus on digitalizing unit interfaces, using optical data transfer technologies (fiber optics), reshaping thermal control approaches, and embedding electrical functionalities into mechanical structures.
This will require to qualify components already common in ground applications including passive ones like optical fiber harness, digital and optical sensors, flat conductors, and we expect to require fewer conventional harness parts.
We encourage our partners to help identify and suggest components that could further help us minimize interconnections.
Given the difficulty of qualifying such technologies within a program's timeframe, Space Agencies support is essential to advance technology readiness levels (TRL) and make them acceptable for project managers in first flight applications.

## Slide 20: It takes time to change but it is time to change!
Passive components will be key contributors.
school notebook
1969 - Apollo Command Module
2024 - Nasa Space Launch System
Command module on mockup stand – ref: APOLLO SPACECRAFT NEWS REFERENCE – Space Division of North American Rockwell Corp
https://commons.wikimedia.org/wiki/File:Em-1_intertank_cables.jpg
Me
in 1969!

## Slide 21
Thank you for your attention
Your questions are welcome!
Contact: Marc.malagoli@airbus.com