## Slide 1
Introduction to
MINCOR - Minimisation of crystal oscillator cosmic radiation effects
Nicolas GUFFLET, Laurent COUTELEAU, Frederic VITTRANT / RAKON
Yannick PADIE, Alexandre ROUSSET / TRAD
ESA contract No. 4000133592/20/NL/FE
5th SPACE PASSIVE COMPONENT DAYS - SPCD 2024
15-18 October 2024 | ESA/ESTEC
Noordwijk, The Netherland

## Slide 2
Quartz resonators and oscillators
Radiations in space & mission profiles
Literature review & radiation sensitivity
Design of Experiment
Progress and results achieved up to now
Conclusion and perspective
Table of content

## Slide 3
Quartz resonators are passive electronic components made of quartz crystal that present electrical resonances from few MHz to some hundreds MHz
They present inherent high stability and Q-factor
Quartz resonators
Electrical equivalent circuitry
Symbol
Quartz resonators of different sizes
Electrical resonance peak around one resonance

## Slide 4
They work using the piezoelectric property of quartz material that permits electro-mechanical coupling.
Electrical resonances corresponds in fact to mechanical resonances
They do not resonate indefinitely. After an initial excitation the signal will decay (the higher the Q factor the longer time to decay)
Quartz resonators
Quartz resonator
Amplitude of the vibration after an initial excitation

## Slide 5
Quartz Oscillators are active devices that sustain the quartz resonance by locking the resonator frequency
They produce a precise and stable frequency signal
They are used in many systems where there is a need of time and frequency control (radar, GPS, communication,…)
For higher stability oscillator (OCXO), the quartz resonator is heated at its turnoverpoint
Quartz oscillators
Quartz oscillator and its output signal
Frequency Temperature curve of a typical resonator
(source: John Vig Tutorial)

## Slide 6
Rakon produces different oscillator types from which the ones dedicated for space market
Oscillator for Space

## Slide 7
Space radiation is made up of three kinds of radiation:
  particles shot into space during solar flares,
  galactic cosmic rays and
  particles trapped in the Earth’s magnetic field.
They are composed of electrons, protons, neutrons, heavy ions and gamma rays
Radiations in space
Van Allen belts
Sun
Extra galactic
(pictures source: NASA)

## Slide 8
Ionization Dose
  Instantaneous dose rate : expressed in rad per unit of time
  Total Ionisation Dose : integration of the instantaneous dose rate over mission life
Non Ionization Dose
  Instantaneous : expressed as Displacement Damage Equivalent Fluence (DDEF) in n/cm²/s
  Total Non Ionisation Dose : integration of the DDEF over mission life expressed in n/cm²
Single Event Effects
  Are not considered here as not applicable to quartz resonators
Characterization of radiations on devices

## Slide 9
As the radiation depends of the position in space, it depends then on the mission profile.
For the study, 6 profiles were considered:
Mission profiles considered
Deep Space
Telecom GEO
Telecom LEO
LEO SSO
GNSS MEO
MEO O3B

## Slide 10
Radiation profiles were determined by TRAD over the life of each mission using OMERE software developed with support from CNES
Low dose, TID and TNID evaluation
Dose rate during the mission
Mission profiles
TID
TNID
OMERE software

## Slide 11
Example of the GNSS MEO mission*:
Dose rate mapping
Dose rate mapping for GNSS MEO orbit. 3D view (left) ; Planisphere view (right)
(*3mm aluminum shielding was considered)

## Slide 12
Example of the GNSS MEO mission*:
Dose rate statistics over the mission life
Histogram of the dose rate data for GNSS MEO mission.
(*3mm aluminum shielding was considered)

## Slide 13
Total Ionization Dose was calculated, below represented as a function of shielding:
Total Ionization Dose
Total dose depth curve for the Navigation GNSS MEO (Galileo, Beidou) orbit

## Slide 14
Total Non Ionization Dose could also be calculated represented below as function of shielding
Total Non Ionization Dose
Displacement Damage Equivalent Fluence in 1 MeV Neutrons as a function of Al shielding for the different missions studied

## Slide 15
Deep litterature review was performed on the subject of radiations and quartz (240+ articles)
Litterature review
1921: Invention of quartz oscillator (Cady)
1845: hydrothermal growth of crystal
WW II
WW I
1956: Commercial process quartz bar growth (Sawyer)
1976: Industrial sweeping of quartz bar
1880: Discovery of piezoelectricity (P&J Curie)
1898: Discoloration of quartz submitted to cathodic ray (Villard)
Sweeping
studies
Low dose effects studies
RAKON studies, articles and production of Ultra Stable Oscillators for space applications.
Work with CNES & SICN/GEMMA
1979:
RAKON ESCC3501 certification
Shortage on natural quartz essentially from brazil
Synthetic timeline around quartz resonators radiation sensitivity
Increased interest for radiation sensitivity because of Nuclear Weapons and Space
1945:
Radiation effect on quartz resonator frequency (Frondel)

## Slide 16
Main physical phenomena affecting the frequency are the following:
Mass loading: additional weight on the quartz lens will decrease the frequency. This phenomenon can occur through oxidization of the electrode for instance. The order of magnitude of this phenomenon is 1ppm frequency drift per atomic layer. Resonators are especially sealed under secondary vacuum level to avoid further evolution.
Mechanical stress: the stress will affect the frequency through the change of the effective elastic constant driving the mechanical wave. Temperature gradient, barometry or acceleration for instance may change the stress of the vibrating part. For acceleration sensitivity the order of magnitude is 1ppb per g.
Quartz material variations: as the velocity of the wave depends on the material constants change in material will affect the frequency. Material used are synthetic materials that present very low level of defects and very low impurities (typically <1ppm)
Frequency sensitivity – primary root causes

## Slide 17
Radiation sensitivity characteristic
  Low dose rate can generate quite strong frequency drift that return back after radiation is off
  TID tends to stabilize the frequency and the dependency to radiation
  TNID not considered as its impact is low on the frequency
Rootcauses
  Quartz material quality clearly a key point in radiation sensitivity.
  Low Dose Rate Sensitivity however not well understood.
  Possibly due to mechanical stressed induced by charge accumulations in surface, subsurface and electrode defects.
Bibliography review outcome w.r.t. radiations sensitivity

## Slide 18
From quartz bar to oscillator

## Slide 19
Considering the New Space market and the technical aspects, RAKON chose to study:
3 enclosures : T807, T1507 and SMD
2 quartz cuts: AT-cut and SC-cut
3 frequencies: 10, 50 and 100MHz
4 different materials: THQ, HQ SW, HQ, SQ. The THQ material is the Cristal Innov material considered as a reference material for the study. HQ and HQ SW are respectively High Quality and High Quality Swept material, SQ is Standard Quality material.
3 electrodes materials: aluminum, silver, gold
2 kinds of sub-surfaces preparation
2 kinds of cleaning
Given the number of possible combinations, the most meaningful combinations were chosen leading to:
6 variants for T1507 10MHz SC-cut resonators
8 variants for T807 100MHz AT- and SC-cut resonators
1 variant for SMD 50MHz AT-cut resonators
Test vehicles of the Design Of Experiment

## Slide 20
Given the precision required the resonators must be measured in oscillators
However, oscillator parts must be protected from radiation to avoid induced effect in electronic
As the gamma radiation source cannot be turned ON/OFF a movable shield is used
Principle for Low Dose Rate sensitivity measurement
Oscillator structured so as to expose ony the resonator in the beam
Fixed screen used to hide electronic parts from the beam and movable screen to perform the LDR cycling
Fixed screen
Moveable screen
Beam
Gamma ray source

## Slide 21
Lead wall (fixed and moveable) were designed
Oscillators were designed and adapted for each enclosures and frequencies
Design of the parts
Test oscillators
Lead walls

## Slide 22
Low dose test system
Motorized shield open
Motorized shield closed
Image of the source from the lead wall
Oscillators plugued behind the lead wall
Image of the lead wall from the source
Measurement system out of the bunker

## Slide 23
Resonators were produced as per specification on the ESCC3501 qualified line
In total, 200+ resonators were produced over the 15 groups with all corresponding datapackages
In each group, 4 pieces were selected as considered to be representative
i.e. 60 resonators in total available for the next steps
60 oscillators manufactured from which 24 are up and ready
Production of resonators & oscillators
Image of resonators from one of the 15 groups

## Slide 24
All materials are presenting quite low level of impurities (<1ppm)
Cristal Innov material being the purest one
Results of impurities analysis
Impurities ions in the different materials (in ug/g)

## Slide 25
To adress the expressed problematic following test plan will be applied :
Test plan
Low dose rate Cycling
Few rad/h
Exposure 20min
Non exposure 100 min
8 cycles - 16 hours
High dose deposition
on resonator
180rad/h
7 days 30kRad
Low dose rate Cycling
Few rad/h
Exposure 20min
Non exposure 100 min
8 cycles - 16 hours
High dose deposition
on resonator
180rad/h
7 days 30kRad
Low dose rate Cycling
Few rad/h
Exposure 20min
Non exposure 100 min
8 cycles - 16 hours
Device characterization
Device characterization
Device characterization
Device characterization
Device characterization
Device characterization
Continuous measurement
Continuous measurement
Continuous measurement

## Slide 26
In this presentation we exposed the objective of the MINCOR project, and the work done up-to-now:
resonator and oscillator types relevant for the study were determined based on market study,
mission profiles and their corresponding radiation level over mission life were determined,
following a literature review, material and process variants to be studied were determined,
different quartz materials were analyzed confirming the state-of-the-art level of Cristal Innov material,
resonators needed for the irradiation study were produced, screened and tested,
a suited method for assessing resonator performance without perturbation by the oscillator was developed and
a test plan was defined
Next steps are ongoing with the measurement of the Low Dose rate behavior of the 60 resonators. First results are expected in last quarter of 2024.
Conclusion & perspectives

## Slide 27
Thank you !
www.rakon.com
Equipment • Subsystems • Oscillators • Filters • Resonators