## Slide 1: CAD-to-FAB, Smiths Interconnect, Dundee
SPCD, ESTEC Noordwijk, 15-18th October 2024
No licence required

## Slide 2: Smiths Interconnect Dundee, Scotland
  AS9100 accredited site established in 1969 as Ferranti
  Becoming TRAK in 1992
  A Smiths Company since 2004
  Microwave & RF established reliability passive components and assemblies have been designed and produced on site for 55 years.
    Isolators & Circulators
    Couplers
    RF filters
  Employing 74 people in a 4,000 m2 facility.
  >30 years of space flight heritage delivering over ~240,000 flight.
  We are proud to share that we have EEE and equipments aboard
    44 deep space missions for ESA, NASA, JAXA & ISRO (most recently Europa Clipper)
    ~700 orbiting platforms in LEO/GEO & MEO

## Slide 3: Problem statement
Traditional RF components, even produced using automation, are ill-suited to a high-mix/ low volume environment, tending to result in prolonged developments, high prototyping costs, large MOQs, and extended production lead-times.
In contrast, direct, computer-controlled manufacturing techniques, additive (e.g., 3D printing) or subtractive (computer-controlled machining or patterning) have flat cost vs. volume curves essentially proportional to the time on the machine and irrespective of the exact nature of the parts being fabricated.
€
€€
€€€
10
100
1000
10000
100000
1000000
Digital manufacturing
Traditional
manufacturing
Cost per unit
Throughput
SPCD, ESTEC Noordwijk, October 2024

## Slide 4: CAD-to-FAB investment motivation
SWaP-C (size, weight, power and cost) is driving the need for the integration of passive functions including ferrite isolators/circulators, RF filters and couplers as components or as multi-function assemblies.
We report initial results of a novel digital manufacturing process combining both substrative and additive computer-controlled fabrication of planar passive RF devices.
We refer to this capability as CAD-to-FAB.
  The prototype CAD-to-FAB system is up and running.
  The full-scale system is on schedule to be commissioned in SINT Dundee by Q1 CY2025 and represents a 2.8M€ investment.
This new manufacturing capability has been used to realise high-performance passive RF components operating in S to K-Bands - the end stop of the capability is expected to be 40-50GHz (TBC).
  currently being focused on developing SMT components operating from C to Ka-bands enabling the economies of scale required for BFN and radar arrays for terrestrial and space applications.
SPCD, ESTEC Noordwijk, October 2024

## Slide 5: Planar structures being produced using CAD-to-FAB
“Microstrip” isolators & circulators
Co-planar waveguide or microstrip interfaces
Wire-bondable (Au) or solderable (Ag)
Illustration
  X-Band 50W CW CPWG circulator
Planar RF filters
Co-planar waveguide or microstrip interfaces
Wire-bondable (Au) or solderable (Ag)
Illustration
  X-Band SMT bandpass filter
RF couplers
SMT/ packaged directional, hybrid, Wilkinson etc
Wire-bondable (Au) or solderable (Ag)
Illustration
  S-Band 30dB directional coupler
SMT isolators & circulators
C to Ka-Band
Illustration
  C-Band SMT isolator with printed termination
Robotic assembly
Automated assembly
Generation 1 assembly COBOT to be replaced in December 2024 with automated pick and place capability
Integrated assemblies
Co-planar waveguide or microstrip interfaces
Wire-bondable or solderable
Illustration
  Ku-Band 2-channel isolated combiner
SPCD, ESTEC Noordwijk, October 2024

## Slide 6: CAD-to-FAB overview
Aimed at creating a cost-effective, automated production capability to produce planar, passive
  Microstrip & SMT non-reciprocal single & dual-junction devices.
  “Printed” and suspended substrate stripline RF filters.
  Couplers and power combiners/ splitters.
  Multi-Function Assemblies (MFAs) combining the above.
Driving this investment program was the desire to
  Leverage the digital manufacturing paradigm providing economies of scale and faster time-to-market.
  Develop new classes of highly customised products.
  Create substantial and scaleable production capacity.
  De-sensitize the business to potential supply chain “insecurity” by “on-shoring” critical production processes.
SPCD, ESTEC Noordwijk, October 2024

## Slide 7: CAD-to-FAB: 1st of class component
C-Band 25Wpk SMT isolator

## Slide 8: CAD-to-FAB example: C-Band SMT 25Wpk isolator
Raw ferrite is procured in wafer form.
  Low Kerf angle “Holes” and “slots”, which will later become ground vias or SMT RF signal interfaces, are created.
  Metallisation, dependent on whether wire-bondable or SMT interfaces are required, is applied to the wafer.
SPCD, ESTEC Noordwijk, October 2024
Raw ferrite wafer or substrate (procured)
Creation of holes & slots: example of ferrite wafer with 300um diameter holes and 600um length oval slot.
Wafer metallization: based on Au or Ag
SMT
WIRE BONDABLE
300um
600um

## Slide 9: CAD-to-FAB example: C-Band SMT 25Wpk isolator
Resistive elements: where required, terminations or resistors are applied before the wafer is singulated.
CAD-to-FAB v1.0 singulates at this stage.
  CAD-to-FAB v2.0 (the full-scale production system) will singulate, using automated dicing, at the final stages of assembly.
SPCD, ESTEC Noordwijk, October 2024
Raw ferrite wafer
~2 x 2 inches
Resistive elements are deposited (where required)
Wafer with 50 Ohm terminations added
Singulated tiles before patterning
Metallization on 2 faces

## Slide 10: CAD-to-FAB example: C-Band SMT 25Wpk isolator
Metallisation is removed from both faces to create the RF pattern, “written” to an accuracy of +/- 5 um.
Assembly is fully automated (including epoxy dispensing) - pick and place components are positioned to +/-5um accuracy.
Automated machine vision inspection is employed during assembly and on the final assembled product.
RF testing will be undertaken on a sample testing basis.
SPCD, ESTEC Noordwijk, October 2024
Pattern creation on both sides of the tile/wafer
Singulated tile pre patterning
Isolator assembled using pick & place
With automated visual inspection, tape & reel

## Slide 11: CAD-to-FAB example: C-Band SMT isolator now in serial production
Compact & low profile
  Size: 13 x 13 x 1.5mm
  Mass: 0.6g max
Consistency
  Tuneless and broadband
  50Ohm dc bleed path
Simplicity
  3 piece-parts excluding epoxy
  Readily produced at scale
Integration friendly
  Tape & Reel packaging
  Reflow solder suitable
  Accurate fiducial markers (x3)
SPCD, ESTEC Noordwijk, October 2024

## Slide 12: CAD-to-FAB example: C-Band SMT 25Wpk isolator – typical test results (+20C, VNA power)
Chart: 
Chart: 
Chart: 
dB
dB
ns
deg.
NB: insertion phase and group delay are plotted over a narrower band
SPCD, ESTEC Noordwijk, October 2024

## Slide 13: CAD-to-FAB example: other products – planar filters, couplers, etc
In addition to non-reciprocal devices realized in either SMT or microstrip, CAD-to-FAB enables
  RF directional, hybrid and Wilkinson couplers as microstrip or SMT devices.
  Planar RF filters (interdigital, coupled line).
    measurements demonstrate that RF filters produced using CAD-to-FAB result in similar RF performances to devices produced using traditional photolithography and wet etching.
  Ultra accurate packaged suspended substrate stripline, coupler circuits
  Multi-functional assemblies of the above
SPCD, ESTEC Noordwijk, October 2024
CAD-to-FAB: coupled line and interdigital SMT filters
100um line width
CAD-to-FAB: illustration of line width capability (thin film)

## Slide 14: CAD-to-FAB example: other products – printed Ku-Band power splitter
CAD-2 FAB ferrite isolator, termination and Wilkinson power splitter
SPCD, ESTEC Noordwijk, October 2024

## Slide 15: CAD-to-FAB SMT Roadmap
This microstrip isolator is the precursor to a SMT solution (17.3-21.2GHz). The SMT version is in development including replacing the hi-resistance termination with a 50 Ohm bleed path type.
Initially limited to C, X, K & Ka-Bands
  C-Band isolator & circulator complete
  X-band circulator _Q3 CY2024
  K-Band isolator _Q4 CY2024
  Ka-Band isolator _Q1 CY2025
No current plans to attempt a classic space qualification approach
  Materials are space qualified
  The process of mounting an SMT part is part of the qualification challenge and cannot be replicated by SINT Dundee
SPCD, ESTEC Noordwijk, October 2024

## Slide 16: SMT Roadmap
SPCD, ESTEC Noordwijk, October 2024
Initially limited to C, X, K & Ka-Bands
  C-Band isolator & circulator complete
  X-band circulator _Q3 CY2024
  K-Band isolator _Q4 CY2024
  Ka-Band isolator _Q1 CY2025
No current plans to attempt a classic space qualification approach
  Materials are space qualified
  The process of mounting an SMT part is part of the qualification challenge and cannot be replicated by SINT Dundee
An SMT isolator targeting 17.3-21.2GHz is the next step

## Slide 17: CAD-to-FAB example: Summary of progress
Observations & notes
Costs are in trending towards expectations using the prototype facility
Electrical characteristics are exceeding expectations generally and especially in terms of consistency
  Primary S-parameters
  Second order parameters – insertion phase and group delay
Capacity is expected to be ~180k planar high mix devices per shift, per annum (microstrip, SMT).
  Non-reciprocal devices
  Filters
  Couplers
  Multi-function assemblies
No additional human resources required as
  Substrate processing, Assembly, and inspection will be fully automated
  Electrical test could be as low as 0.1% or removed altogether for the simplest components.
Next steps (2025)
  Automated test
  Automated tape and reel

## Slide 18: Acknowledgements
Smiths Interconnect acknowledges the support of the United Kingdom Space Agency (UKSA) through its Space Cluster Infrastructure Funding (SCIF) program contributed £1.9M, matched with a similar amount from Smiths Group, enabling the creation of the CAD-to-FAB facility and the expansion of the Smiths Interconnect, Dundee Space Qualification Laboratory.
SPCD, ESTEC Noordwijk, October 2024

## Slide 19
Smiths Interconnect Proprietary Information – For Exclusive Use of the Addressed Party Only